## Slide 1: Diploma in Packaging Technology
Package Line Operations
Notes: Introduction
Welcome
Background to FPC
Important contribution to the food industry

## Slide 2: Contact
Tony Duffy
tony-duffy@outlook.com
++44(0)7526497265

## Slide 3: Overview
Line Requirements
Automation
Layout
Efficiency
Inspection

## Slide 4: Line Requirements
Group exercise
When deciding on a new packaging line what information is required on
  Product
  Packaging
  Operational requirements
  Equipment

## Slide 5: Product
Physical format, fragility
Hazards
Hygiene requirements
Variants
Market information

## Slide 6: Packaging Materials
Materials
Style, size, tolerances
Stability, fragility,
Variants
Other critical performance indicators

## Slide 7: Operational
Output, speed, automation
Run lengths
Space and layout constraints
Labour requirements, skill and numbers
Health & Safety
Time constraints

## Slide 8: Equipment
Services & Space
Integration
Training requirements
Lead times and installation
Commissioning & Performance assessment

## Slide 9: Automation Impact

## Slide 10: Automation Impact
Speed, quality, consistency, tolerances, adjustments
Hygiene & safety
Labour and skill requirements
Capital cost
Flexibility
Integration

## Slide 11: Production Layout
Process layout (job shop)
Product Layout (production line)
Hybrid
Fixed position

## Slide 12: Process layout
Group similar processes together.
  Cooking, mixing, chopping
  Printing, die cutting, folding gluing
Prioritise workload with available equipment / staff
General machines capable of producing a variety of products
Layout of economic activity centres important

## Slide 13: Product layout
Lines for individual products / families
Product flows through production
Resources arranged about product path
Specialized
Straight, U, S,

## Slide 14
Elements of Process and Product
Group technology
  Families of products with similar requirements
  Technology arranged around product requirements
Product stays in one place
All equipment and parts brought to product
Hybrid
Fixed Position

## Slide 15: Process evaluation
Issues to consider in process packaging line review.

## Slide 16: Process evaluation
Material handling
Production rate
Specialization
Flexibility
Capital expenditure
Work environment
Work in progress
Product variety

## Slide 17: Economic activity areas arrangement
Cross contamination
  Product, people, air, water, waste
Efficiency
  Movement of materials, equipment, people
Storage
  Raw materials, work in progress, finished goods, equipment, locations

## Slide 18: Economic activity areas arrangement
Space
  Routine and non routine tasks.
  Work in progress
  Circulation
Hygiene
  People, equipment, facilities

## Slide 19: Filling Lines
Tend to be production lines (product layout)
Separate machines linked together
Balancing speeds
  Higher speeds feeding into and out from critical plant (often filler)
  Dynamic speed adjustment or on/off

## Slide 20: Packaging Line Efficiency
How do we measure line efficiency?
Why do we measure efficiency?
What factors effect line efficiency?

## Slide 21: Efficiency
Efficiency
  Ration of Output to Input
  Operating time to available time
  Output rate to target

## Slide 22: Equipment Speed
Design speed
  Theoretical max speed
Capacity
  Upper sustainable limits
Running speed
  Instantaneous operating rate
Output rate
  Output of acceptable product per given time

## Slide 23: Equipment Efficiency
Output required
  Running speeds
  Wastage
  Breaks, product changes
  Maintenance & breakdown
  Operating / shift pattern

## Slide 24: Output
Speed & Machine Operation
  50 cpm, at 98% efficiency: 49 cpm
  70 cpm at 65% efficiency: 46 cpm

## Slide 25: Accumulators
Provide product storage
Isolate key areas
Placed after non interruptible operations
  Ovens
  Curing
NOT to be used to compensate for defective machines
The third generation of the Accutable (youtube.com)

## Slide 26: Accumulators
Space requirements
Sequences
  FIFO
  LOFO
  https://www.youtube.com/watch?v=y6_tuxycJ2M

## Slide 27: Line output
Unscrambling: 110 pack/min 96% eff
Filler: 90 pack/min 95% eff
Labeller: 110 pack/min 97% eff
Shrink Wrap: 120 pack/min 92% eff

## Slide 28: Line output
Unscrambling: 110 pack/min 96% eff
Filler: 90 pack/min 95% eff
  Accumulator
Labeller: 110 pack/min 97% eff
Shrink Wrap: 120 pack/min 92% eff

## Slide 29: Line Efficiency
Labeller stopped
  Filler can continue to run

## Slide 30: Line output
Unscrambling: 110 pack/min 96% eff
  Accumulator
Filler: 90 pack/min 95% eff
Labeller: 110 pack/min 97% eff
Shrink Wrap: 120 pack/min 92% eff

## Slide 31: Line output
Unscrambling: 110 pack/min 96% eff
Filler: 90 pack/min 95% eff
Labeller: 110 pack/min 97% eff
  Accumulator
Shrink Wrap: 120 pack/min 92% eff

## Slide 32: Line output
Unscrambling:
    Accumulator – Output rate
Filler:
    Accumulator – Output rate
Labeller:
    Accumulator – Output rate
Shrink Wrap:

## Slide 33: Overall Equipment Effectiveness
Linked to total productive maintenance (TPM)
  Downtime losses (availability)
  Speed losses (performance rate)
  Defect loss (quality rate)
OEE = Availability x Performance rate x Quality rate

## Slide 34: OEE
Availability (87%)
    Examples
Performance (93%)
    Examples
Quality (95%)
    Examples

## Slide 35: Line Speeds
Straight Machines
  Indexing to position, single or multi head
  Up to 150cpm
Rotary Machines
  High speed, large number of heads, compact
  Up to 2000cmp

## Slide 36: Line speed
Container shape
Shingling
  Cylindrical / oval / square
Stability
  Base, weight, points of contact
Optimum speed?

## Slide 37: Changeovers
From last saleable product to first saleable
Time reduction
  Preparation. Parts, tools operators, duplicates
  Changeover. No tools,
  Set up. Adjustment
  Trial. Run up to production speed

## Slide 38: Changeovers
https://www.youtube.com/watch?v=aHSUp7msCIE

## Slide 39: Availability
Planned preventative maintenance
  Time or work based
  Condition based
  Opportunity based
Breakdown maintenance
  Availability of parts
  Damage to products

## Slide 40: Quality
Cannot be inspected in
Determine appropriate checks
Monitor process
Feedback to operators
Self inspection

## Slide 41: Inspection
Inspection frequency
  Product category
  Level of risk
  Established inspection systems
  Inspection cost
  Due diligence

## Slide 42: Inspection
Weights
Contamination – Foreign body
Leakage
Correct product / pack
Coding & traceability

## Slide 43: Other Quality Checks

## Slide 44: Online v’s Offline Inspection
Online
  100 % inspection
  Automated possible
  Reliability
  Capital
  Line speed
  Operator training
Offline
  Statistical based
  Destructive testing
  Cost
  Training requiement

## Slide 45: Inspection Feedback
Statistical Process Control (SPC)
  Process capability
  Reduction of variation
  Not related to product tolerances
Requires action

## Slide 46: Overall Equipment Effectiveness
Availability
Performance
Quality
OEE = Availability x Performance rate x Quality rate